## Slide 1: Cognitive Robot Programming using Procedural Parameters and Complex Event Processing
2016 IEEE International Conference on Simulation, Modeling, and Programming for Autonomous Robots
Session W-3: Machine Learning and Middleware for Robotics
Floris Erich, Kenji Suzuki
University of Tsukuba

## Slide 2: Research overview
Drawbacks of having seperate developer, operator and therapist:
Higher cost
Slower speed due to coordination overhead
Higher chance of errors being made
Hence, ideally the therapist would be able to develop and operate the robot on his own
Conducting
Robot
Subject
interaction
Experiment area
User (therapist)
feedback
An experiment in Socially Assistive Robotics
Preparation
Developer
writes software for
Operator
interaction
commands
instructions

## Slide 3: Research objectives
Expand the programming capabilities of end-users
Evaluate the usage of the reactive paradigm for robotics
Implement a robot control architecture based on the reactive paradigm
Contribution of this paper:
  Implemented a concrete example robot application using the reactive programming paradigm

## Slide 4: Related work: Choregraphe
Graphical interface for programming robots from Softbank
Components are called boxes and have input and output ports
Special ports for starting, stopping and pausing a box
Boxes can contain a subgraph, Python code or a choreography
Box
Output Port
Output Port
Start Port
Data Port
Stop Port

## Slide 5: Related work: Targets-Drives-Means (Berenz and Suzuki, 2014)
Hybrid deliberative / reactive architecture (Arkin, 1998)
Focused on end user development
Schemas are representations of external properties
Programs execute behaviors when their schema is active
If multiple behaviors are to be executed their execution is prioritized using a score calculator
Behaviors execute action units
Action units are pairs of an actuation function and an activation condition
Functions are called if their condition applies
Schema
Behavior
Action unit
Function
Condition
Score calculator
Program

## Slide 6: Related work: Robot Operating System (Quigley et al., 2009)
Collection of packages and tools for controlling robots
We are mainly interested in the ROS Graph
Nodes are units of computation
Nodes communicate using messages
Messages are passed using topics
Node n
Topic t
Node n’
1. subscribe
2. publish
3. push

## Slide 7: Related work: DisCODe (Stefanczyk and Kornuta, 2014)
Distributed Component Oriented Data Processing
Behavior is contained in components
Components are connected using arrows

## Slide 8: Cognitive Robot Programming
Robot
Environment
sensing
actuation
Software
input
output
Robots are embedded into a partly uncontrollable environment
The alignment between an environment, the robot hardware and the robot software is complex
Notes: Dexterous robots are robots embedded into an environment
A robot can receive stimuli from the environment (sensing) and send a response back (actuation)
Software receives stimuli from the robot, performs cognition, and sends the response to the robot
The DevOps approach can be used to support alignment of the software with the hardware embedded into an environment

## Slide 9: Complex Event Processing
Low level robot behaviors can be separated into three tasks (Arkin, 1998):
  Sensing
  Computation/planning
  Acting
Typically components are created for each task and connected using middleware
Push behavior can be created using the Observer Design Pattern (Gamma et al., 1994)
The observer pattern can be extended to function over streams of events instead of single items (Maier and Odersky, 2012; Meijer; 2012)
Data flow between components is specified using connectors (Taylor, Medvidovic and Dashofy, 2008)

## Slide 10: CEP Graphical Representation
We propose a graphical representation for designing and developing low level robot behaviors: The CEP Graph

## Slide 11: Procedural parameters
Most operations accept a procedure as parameter
The operator specifies what should be done
The procedural parameter specifies how to do it
Procedures are higher order functions (Hutton, 2016)
  We can treat the functions as any other variable
Simple example (pseudocode):
numbers = [1…10] [1,2,3,4,5,6,7,8,9,10]
square = Integer => Integer
numbers.foreach(square) [1,4,9,16,25,36,49,64,81,100]

## Slide 12: Architecture
Control PC
NAO
naoqi
DCM
Reactive Extensions2
IPython1 Notebook
Sensor
Sensor
Sensor
Sensor
Sensor
Actuator
CEP Graph
1: www.ipython.org
2: https://github.com/ReactiveX/RxPY

## Slide 13: Example application
Make the robot:
  Track far away objects with its head
  Track medium distance objects with its head and its body
  Track close distance objects with the arm closest to the object

## Slide 14: Demonstration

## Slide 15: Intuitive implementation
Object
Head tracker
Head and body tracker
Arm tracker
far away
medium distance
close

## Slide 16: Intuitive implementation: Object distance
Ball
Head
Head + body
Arm
Ball distance > 50 cm
Ball distance > 20 cm and <= 50
Ball distance <= 20 cm

## Slide 17: Intuitive implementation: Left or right arm
Ball
Head
Head + body
Left arm
Ball distance > 50 cm
20 cm < Ball distance 50 cm
Ball distance 20 cm
Ball left of torso
Right arm
Ball right of torso

## Slide 18: Implementation: Sampling
Avoid that the robot changes tracking modes too many times in a certain time period
Reduce the amount of computation
(d) Sample: On an interval specified by the sample rate, take the latest value from the input stream and put this into the output stream
Ball
BallSamples
sample(50)

## Slide 19: Implementation: Distance to ball
size = …
def dist2(width, height):
return (1/4.) ∗ ( size/tan(width) + size/tan(height) )
def ball_distance(ball):
return dist2(ball.width, ball.height)
BallSamples
Distance
map(ball_distance)

## Slide 20: Implementation: Filter based on distance
Separate the stream into multiple streams based on distance to the ball
  Far: Distance > 50 cm
  Medium: Distance > 20 cm and distance 50 cm
  Close: Distance 20 cm
Distance
Head + body
Head
Arm
filter()
filter()
filter()

## Slide 21: Implementation: Determining the arm
Transform ball location in camera frame to torso frame
We only need to know if the horizontal position is to the left or to the right of the torso
Simple solution: Take the sum of the angle of the head yaw and the ball angle
(e) CombineLatest: Whenever an item gets added to an input stream, takes the latest values of all input streams and applies the values as arguments to λ. Puts the result in the output stream.
BallSamples
Head yaw
map()
filter()
map()
BallX
combine()
map()
Arm

## Slide 22: Implementation: Dealing with old data
CombineLatest takes the latest value from a set of streams
There can be a large time difference between the insertion times of the item in each stream
Head yaw always contains the most up to date value, but the value of the ball stream might be outdated
Head yaw
BallX
combine()
map()
Arm
Head yaw
BallX
combine()
map()
Arm
timestamp
timestamp
filter()

## Slide 23: Implementation: Controlling the trackers
Assume we have the following actuation modules:
  head_tracker: On input switches tracking mode to head
  head_body_tracker: On input switches tracking mode to head and body
  arm_tracker: Takes as input a string representing the arm to use, switches to tracking with that arm
head_tracker
head_body_ tracker
arm_tracker
Arm
Head + body
Head
subscribe
subscribe
subscribe

## Slide 24: Complete implementation

## Slide 25: Discussion and conclusion
CEP with Procedural Parameters reduces boilerplate code and standardizes terminology using operators
  Less developer effort
  Less bugs
Solution is suitable for developing mid level robot behaviors
  Currently we are exploring integration with high level behavior engines
  Low level modules such as sensors, actuators and complex operations are supplied by a library created by robotics experts
We have shown the approach works through a simple example
  Performance with more complex programs needs to be evaluated
  Intuitiveness of the approach has to be validated through a user study

## Slide 26: References
R. C. Arkin, Behavior-based Robotics, 1st ed., Cambridge, MA, USA: The MIT Press, 1998.
V. Berenz and K. Suzuki, “Targets-drives-means: A declarative approach to dynamic behavior specification with higher usability,” Robotics and Autonomous Systems, vol. 62, no. 4, pp. 545–555, 2014.
E. Gamma, R. Helm, R. Johnson, and J. Vlissides, Design Patterns: Elements of Reusable Object-Oriented Software. Addison-Wesley Professional. 1994.
G. Hutton, Programming in Haskell, Second Edition. Cambridge University Press. 2016.
I. Maier and M. Odersky, “Deprecating the Observer Pattern with Scala.react,” Tech. Rep., 2012.
E. Meijer, “Your mouse is a database,” Communucations of the ACM, vol. 55, no. 5, pp. 66–73, May 2012.
M. Quigley, K. Conley, B. P. Gerkey, J. Faust, T. Foote, J. Leibs, R. Wheeler, and A. Y. Ng, “Ros: an open-source robot operating system,” in ICRA Workshop on Open Source Software, 2009.
M. Stefanczyk and T. Kornuta, “Handling of asynchronous data flow in robot perception subsystems,”, SIMPAR 2014.
R. N. Taylor, N. Medvidovic and E.M. Dashofy, Software Architectures: Foundations, Theory and Practice”, John Wiley & Sons, 2008.